## Slide 1
Project Proposal and deliverables
11-Dec-2019
C. Fischer-Rasokat

## Slide 2
Instrument Design
Labi Quant Systems
Front View
Labi Quant Systems
Front View with open drawer
Labi Quant Systems
Rear View

## Slide 3: LQS: Perfect fit for reflective lateral flow test and color change tests
  5 Mpix. black/white camera (8 Bit)
  Multi color illumination to recognize color change tests
  Optimized Software for Lateral Flow tests
  Calibration and Self-adjustment among internal reference material
  High Performance CPU for quick response
  QC material for external routine checks
  Low Inter device variation < 3% CV
  High reproducibility between different readings < 0.5% CV
  Dot detection (300µm diameter)

## Slide 4: LQS: Perfect fit for reflective lateral flow test and color change tests
  4,3´´ touch display
  Intuitive workflow with few user interactions
  Fully barcode supported test and patient ID entry
  User centric design among DIN EN ISO 9241-210
  Many customization options

## Slide 5: Consequent focus on Barcode Input
Method file on barcode card:
Measurement parameter
Evaluation parameter
Calibration values
Reader:
Imports method file via separate menu

## Slide 6: LQS: Perfect fit for reflective lateral flow test and color change tests
Internal/External Barcodereader
  Read method file via 2D Barcode
  Read Patient ID via external1D/2D Barcode
USB ports
  Plug and play printer and barcode reader
  Export Raw Data files on USB stick
Ethernet
  Connection to LQS connect SW
  LQS connect as local data management system or
  LQS connect as adapter to LIS,KIS, middleware or physician office management software
  HL7 and other communication protocols feasible